## Slide 1
CSE 4105 · SYSTEM PROGRAMMING
Lecture 3.3
Machine-Independent Features
and assembler design options
Md Mahbub E Noor
Assistant Professor, Department of CSE
University of Barishal
countc.obj (control sections)
HMAIN 000000000019
DTEXT 000013TEXTEND000019
RCOUNTA
M00000405+COUNTA
…
M00002506+TEXTEND
M00002506-TEXT

## Slide 2: What you will learn today
Use literals and LTORG, and show where the assembler places them (LITTAB).
Define symbols with EQU and expressions, and tell absolute from relative ones.
Explain program blocks and control sections, and read D, R and M records with symbols.
Compare one-pass, two-pass and multi-pass assemblers, and patch forward references.
Today's plan (60 min)
0–5
Recap of Lecture 3.2
5–15
Literals
15–25
EQU and expressions
25–40
Blocks and control sections
40–55
One-pass, multi-pass
55–60
Checkpoint, homework
Adding EQU and literals to your C assembler (slide 22) is the lab.
2 / 26

## Slide 3: Quick recap of Lecture 3.2
Q1
Why is STA TOTAL base-relative in COUNTX?
TOTAL is 4127 bytes away; PC-relative reaches only 2047. So it uses (B) = 1041 with disp 000.
Q2
What does M00002305 mean?
Add the program's start address to the 5 half-bytes starting in byte 0023. Today M records also name a symbol.
Q3
Why do PC-relative instructions need no M record?
They store a distance, and distances do not change when the whole program moves.
3 / 26

## Slide 4: Literals
PART 1
Write the constant where you use it; let the assembler find it a home.
4 / 26

## Slide 5: A literal is the assembler's string constant
C you already write
const char *t = "BANANA";
if (c == 'A') …
/* where does "BANANA" live? */
/* you never named it */
gcc -S lit.c (real output)
.section .rodata
.LC0:
.string "BANANA"
…
leaq .LC0(%rip), %rax
SIC: count with a literal
COMP =X'000041'
ADD =X'000001'
* the assembler makes
* a word for each one
SAME AS C
Same idea as a C string literal
You write the value where you need it. The compiler or assembler creates a hidden, unnamed constant in memory (gcc calls it .LC0) and puts its address into the instruction.
DIFFERENT FROM C
Not the same as # immediate
COMP #65: the value 65 is inside the instruction (SIC/XE only, at most 4095).
COMP =X'000041': the value is in a separate word; the instruction holds its address. Works in plain SIC and for any size.
Book: Beck §2.3.1 (literals)
5 / 26

## Slide 6: LITTAB and LTORG: where literals end up
LOC
source
code
2000
FIRST LDX =X'000000'
042024
2003
LOOP LDA =X'000000'
002024
2006
LDCH TEXT,X
50A030
2009
COMP =X'000041'
282027
200C
JEQ FOUND
302018
200F
NEXT TIX =X'000006'
2C202A
2012
JLT LOOP
382003
2015
DONE J DONE
3C2015
2018
FOUND LDA TOTAL
002036
201B
ADD =X'000001'
18202D
201E
STA TOTAL
0C2036
2021
J NEXT
3C200F
LTORG
2024
* =X'000000'
000000
2027
* =X'000041'
000041
202A
* =X'000006'
000006
202D
* =X'000001'
000001
2030
TEXT BYTE C'BANANA'
42414E414E41
2036
TOTAL WORD 0
000000
Pass 1 meets =X'000041'
Not in LITTAB yet: add it, without an address. A second use of the same literal is not added again.
Pass 1 meets LTORG
Every waiting literal gets the next addresses (2024, 2027, 202A, 202D), like data written right here.
Pass 2
The instruction uses the literal's address from LITTAB: COMP =X'000041' → 282027.
No LTORG?
The literals go after END, at the very end of the program. LTORG lets you keep them near the code that uses them.
Book: Beck §2.3.1
6 / 26

## Slide 7: Symbol definitions and expressions
PART 2
EQU, ORG, and the arithmetic an assembler is allowed to do.
7 / 26

## Slide 8: EQU: the assembler's #define
C
#define MAXLEN 6
enum { A = 0, X = 1, L = 2 };
char text[] = "BANANA";
int tlen = sizeof text - 1; /* 6 */
SIC/XE
MAXLEN EQU 6
RA EQU 0 ; register names
TEXT BYTE C'BANANA'
TEXTEND EQU *
TLEN EQU TEXTEND-TEXT ; = 6
A name for a number
LDT #MAXLEN assembles to 750006, exactly like LDT #6. Change the 6 in one place and every use follows.
A name for an address
TEXTEND EQU * gives TEXTEND the current LOCCTR (here 0039). * means "here".
Computed by the assembler
TEXTEND-TEXT = 0039 − 0033 = 6. The program never computes it at run time; the length is fixed when you assemble.
Book: Beck §2.3.2 (symbol-defining statements)
8 / 26

## Slide 9: Absolute and relative expressions: C pointer rules
Expression | Result | Example | C pointer rule
number | absolute | MAXLEN EQU 6 | an int
label | relative | TEXT | a pointer
label − label | absolute | TEXTEND-TEXT = 6 | p − q is an int (ptrdiff_t)
label ± number | relative | TEXT+3 | p + 3 is a pointer
label + label | ERROR | TEXT+TEXTEND | p + q is not allowed
label × number | ERROR | TEXT*2 | p * 2 is not allowed
gcc -c ptr.c (real)
char *bad = p + q;
error: invalid operands
to binary + (have
'char *' and 'char *')
Why the rule?
When the program moves, a relative value moves too. label − label stays the same, so it is safe. label + label would move twice: no loader could fix it.
Only relative symbols ever need an M record, because only they change when the program moves.
Book: Beck §2.3.3 (expressions)
9 / 26

## Slide 10: Program blocks and control sections
PART 3
Arrange the pieces of one program, or split a program into pieces.
10 / 26

## Slide 11: Program blocks: write in any order, store in groups
countb.asm (parts)
FIRST STL RETADR
…
J @RETADR
USE CDATA
RETADR RESW 1
CNT WORD 0
USE CBLKS
BUFFER RESB 4096
USE CDATA
TEXT BYTE C'BANANA'
USE
FOUND LDA CNT
…
Block | Number | Start | Length
(default) | 0 | 0000 | 0027
CDATA | 1 | 0027 | 000C
CBLKS | 2 | 0033 | 1000
(default) code · 0000
CDATA · 0027
CBLKS · 0033
the program in memory
How it works
Pass 1 keeps one LOCCTR per block. At the end, blocks are placed one after another, and each block's start is added to the addresses inside it.
SAME AS C
Your C program has blocks
size blocks.o (real):
text 170 · data 4 · bss 4128
Code, initialised data and the big uninitialised buffer, kept apart.
Book: Beck §2.3.4 (program blocks)
11 / 26

## Slide 12: The object program of COUNTB
HCOUNTB000000001033
T0000001B172024B410750006B40053A020290041332008B8503B2FF03E200C
T00002A0900000042414E414E41
T00001B0C03200C1900010F20063F2FEC
E000000
Records follow the source, not the addresses: T 000000 (code), then T 00002A (CDATA: CNT and TEXT), then T 00001B (the code after USE). The loader puts each one at its own address; order does not matter.
CBLKS makes no record: BUFFER is RESB: it only adds 1000 to the program length (H: 001033).
No M records: Every instruction is PC-relative or immediate. Putting the buffer last made format 4 unnecessary.
12 / 26

## Slide 13: Control sections: separately assembled parts, like C files
main.c
char text[] = "BANANA";
int counta(void);
int main(void) {
printf("%d\n", counta());
}
counta.c
extern char text[];
int counta(void) {
… count 'A' in text …
}
countc.asm (parts)
MAIN START 0
EXTDEF TEXT,TEXTEND
EXTREF COUNTA
FIRST STL RETADR
+JSUB COUNTA
STA CNT
…
TEXT BYTE C'BANANA'
TEXTEND EQU *
COUNTA CSECT
EXTREF TEXT,TEXTEND
…
+LDCH TEXT,X
LEN WORD TEXTEND-TEXT
C | SIC/XE | Meaning
a .c file | CSECT | a part assembled on its own, with LOCCTR from 0
a global (non-static) definition | EXTDEF | "others may use this name"
extern / a prototype | EXTREF | "this name is defined elsewhere"
nm: T, D | D record | the names this part defines
nm: U | R record | the names this part needs
Book: Beck §2.3.5 (control sections and program linking)
13 / 26

## Slide 14: D, R and M records: the linker's to-do list
HMAIN 000000000019
DTEXT 000013TEXTEND000019
RCOUNTA
T0000000D17200A4B1000000F20063E2000
T0000130642414E414E41
M00000405+COUNTA
E000000
HCOUNTA000000000028
RTEXT TEXTEND
T0000001DB410B44077201EB40053900000290…
T00001D0B01000190043F2FEE000000
M00000A05+TEXT
M00002506+TEXTEND
M00002506-TEXT
E
D Define
DTEXT 000013TEXTEND000019: name + address, for every EXTDEF. Like the T and D lines of nm.
R Refer
RCOUNTA, RTEXT TEXTEND: the names this section needs. Like nm's U lines.
M with a symbol
M00000405+COUNTA: add the address of COUNTA (not of this section) to the 5 half-bytes at 0004.
Two M for one word
LEN WORD TEXTEND-TEXT is assembled as 000000 with M…+TEXTEND and M…-TEXT. The linker adds one, subtracts the other: 0019 − 0013 = 6.
14 / 26

## Slide 15: Assembler design options
PART 4
Must an assembler read the program twice? Is twice always enough?
15 / 26

## Slide 16: One-pass assemblers: remember the holes
A second pass costs time: the whole program is read (or stored) twice. A one-pass assembler writes code at once, and for a label that is not known yet it leaves a hole plus a note: "fill me in later".
1
Data before code
Easy part: define data first, so data references are never forward. Jumps forward (an if, a loop exit) are still possible.
2
A list per symbol
SYMTAB marks an unknown symbol with * and keeps a linked list of the places that used it.
3
Patch when defined
When the label finally appears, walk the list and write its address into every hole.
4
At END
Any symbol still marked * is undefined: an error.
SAME AS C
Like a C linked list
struct fix { int addr; struct fix *next; }; One list per undefined symbol: the same code you wrote in Data Structures.
SAME AS C
Like gcc + ld
gcc's assembler leaves 00 00 00 00 for puts (Lecture 1) and the linker fills it. A one-pass assembler fills its own holes.
Book: Beck §2.4.1 (one-pass assemblers)
16 / 26

## Slide 17: Watch a one-pass assembler fill its holes
Click the video to play or pause. About 75 seconds, no sound.
Watch for
1. Orange code = a hole (address 0000 written).
2. SYMTAB's waiting column: the linked list of holes.
3. JLT LOOP: a backward reference is complete at once.
4. When ZERO is defined, two holes are filled together.
5. At END no symbol is waiting: TOTAL = 3.
17 / 26

## Slide 18: The forward references of COUNT, and their patches
Symbol | Used (holes) at | Defined at | Patched code | Patch as a T record
FOUND | 200C | 2018 | 302018 | T00200D022018
DONE | 2015 | 2024 | 3C2024 | T002016022024
TEXT | 2006 | 2027 | 50A027 | T00200702A027
LENGTH | 200F | 202D | 2C202D | T00201002202D
LETTERA | 2009 | 2030 | 282030 | T00200A022030
ZERO | 2000, 2003 | 2033 | 042033, 002033 | T002001022033 T002004022033
TOTAL | 2018, 201E | 2036 | 002036, 0C2036 | T002019022036 T00201F022036
ONE | 201B | 209D | 18209D | T00201C02209D
Read a patch: T00200D022018 = "at 200D, write 2 bytes: 20 18". It overwrites the 0000 left in JEQ FOUND (302018 at 200C). The loader applies records in order, so the patch wins.
Book: Beck §2.4.1
18 / 26

## Slide 19: When two passes are not enough: multi-pass assemblers
multipass.asm
MULTI START 0
HALF EQU TLEN/2
TLEN EQU TEXTEND-TEXT
FIRST LDA #HALF
J FIRST
TEXT BYTE C'BANANA'
TEXTEND EQU *
our two-pass assembler (real)
line 2: undefined symbol TLEN
(EQU needs every symbol defined earlier)
Why Pass 1 is stuck
EQU must have a value in Pass 1, because it may change LOCCTR-dependent things later. HALF needs TLEN, TLEN needs TEXTEND: both still unknown.
The multi-pass answer
Store HALF = TLEN/2 with the list of symbols it waits for. When TEXTEND (000C) is defined, TLEN = 000C − 0006 = 6 becomes known, then HALF = 3. Each new value can unlock others.
Result
LDA #HALF → 010003. Reordered so a two-pass assembler can do it, our assembler gives exactly this.
SAME AS C
C does the same
enum { HALF = TLEN / 2 }; first → gcc: 'TLEN' undeclared
Book: Beck §2.4.2 (multi-pass assemblers)
19 / 26

## Slide 20: One, two or many passes?
 | One-pass | Two-pass | Multi-pass
Forward jumps and data | patched later (holes) | yes | yes
EQU that uses a later symbol | no | no | yes
Reads the source | once | twice (or once + stored copy) | as often as needed
Extra memory | lists of holes | intermediate file | dependency lists
Typical use | load-and-go, teaching, fast test runs | most assemblers (Beck's SIC/XE, our lab) | rare: complex symbol definitions
C link: a C compiler reads your file once, which is why C makes you declare before use. The assembler takes on that work itself.
Book: Beck §2.4
20 / 26

## Slide 21: EQU and literals in your assembler
LAB 3.3
Version 2 of your C assembler: two new tables and one new directive.
21 / 26

## Slide 22: Lab 3.3 tasks, step by step
1
EQU with a number
MAXLEN EQU 6: put MAXLEN into SYMTAB with value 6. Its LOC column shows 0006.
2
EQU with * and A−B
TEXTEND EQU *, TLEN EQU TEXTEND-TEXT. Write eval(): number, *, SYMBOL, SYMBOL−SYMBOL, SYMBOL+number.
3
LITTAB
struct lit { char text[40]; int addr; int placed; }; Add a literal the first time it is seen.
4
LTORG and END
Give every waiting literal an address and output it like a BYTE line marked *.
5
Pass 2
An operand starting with = takes its address from LITTAB. Test: countlit.asm must match countlit_expected.obj.
6
Break it
Put TLEN EQU TEXTEND-TEXT before TEXT. Your assembler must stop with an error, not print rubbish.
Submit: sicasm_v2.c, the listing and object program of countlit.asm, and the output of task 6.
22 / 26

## Slide 23: Checkpoint: test yourself
Q1
COMP #65 and COMP =X'000041': what is the difference?
→ # puts 65 in the instruction; = makes a word in memory and uses its address
Q2
Where do literals go if there is no LTORG?
→ after END, at the end of the program
Q3
TEXT = 0033, TEXTEND = 0039. Is TEXTEND−TEXT absolute or relative? Value?
→ absolute, 6
Q4
Which C keyword is closest to EXTREF?
→ extern
Q5
Why can a two-pass assembler handle LDA #HALF before HALF, but not HALF EQU TLEN/2 before TLEN?
→ an EQU needs its value in Pass 1; an operand only in Pass 2
23 / 26

## Slide 24: Key ideas from today
A literal is a hidden, unnamed constant, like a C string literal. LTORG says where to put the pool.
EQU names a value. label − label is absolute; label + label is an error, like C pointers.
Program blocks: one LOCCTR per block, then the blocks are stacked: C's .text, .data, .bss.
Control sections are assembled apart, like .c files. D, R and M+symbol records tell the linker what to join.
One-pass: leave holes and patch them. Multi-pass: resolve symbol definitions that point forward.
Your C assembler now has OPTAB, SYMTAB, LITTAB and an expression evaluator.
24 / 26

## Slide 25: Homework 3.3 (due before Lecture 4)
1. Literals
Rewrite sumn.asm (Lecture 3.1) so it uses literals instead of ZERO and N. Assemble it by hand: LITTAB, listing, object program.
2. Expressions
With TEXT = 0033, TEXTEND = 0039, MAXLEN = 6: is each legal? Absolute or relative? TEXTEND-TEXT+MAXLEN, TEXT+MAXLEN, MAXLEN-TEXT, TEXT+TEXTEND-TEXT.
3. Blocks
Move BUFFER RESB 4096 in countx.asm into its own block with USE. Which instructions no longer need format 4 or base-relative addressing?
4. One pass
Run the one-pass method by hand on sumn.asm. List every hole and the patch T record for each.
5. C
Write main.c and counta.c (slide 13) yourself. Run nm and readelf -r on both .o files and match each line to a D, R or M record of countc.obj.
25 / 26

## Slide 26: Next lecture and reading
NEXT: LECTURE 4
Macro processors
Teaching the assembler new instructions: macro definition and expansion (NAMTAB, DEFTAB, ARGTAB).
The C preprocessor and #define as a real macro processor: gcc -E.
Main text
L. L. Beck, System Software, 3rd ed. Today: §2.3 and §2.4. Read §4.1 before Lecture 4.
C side
CS:APP, 3rd ed., §7.5–7.6 (symbols and symbol resolution): EXTDEF/EXTREF in ELF.
Tools
nm, readelf -r, size on the lab PC: try them on any .o file.
Lab files
lab3_files.zip: countlit.asm, countl.asm, countb.asm, countc.asm, blocks.c, main.c, counta.c.
26 / 26