## Slide 1
CSE 4105 · SYSTEM PROGRAMMING
Lecture 13
Interrupts and Exceptions
the IDT, IRQs, bottom halves, timers
Md Mahbub E Noor
Assistant Professor, Department of CSE
University of Barishal
./exc (real)
7 / 0 -> FPE trap 0
ud2 -> ILL trap 6
hlt -> SEGV trap 13
read *NULL -> SEGV trap 14 err 0x4
# the CPU's own numbers, seen from C

## Slide 2: What you will learn today
Classify events that stop the CPU: interrupts, traps, faults and aborts.
Explain the IDT and what the CPU saves when an exception or interrupt arrives.
Follow a disk interrupt from the device to the woken process, with real traces.
Explain top and bottom halves (softirqs, workqueues) and kernel timers.
Today's plan (60 min)
0–5
Recap of 12.2
5–12
Three ways in
12–25
Exceptions, the IDT
25–40
Device interrupts
40–50
Bottom halves
50–55
Timers
55–60
Lab, checkpoint
Lab 13: irqtop.c, a top for interrupts.
2 / 32

## Slide 3: Quick recap of Lecture 12.2
Q1
Where is an ext2 superblock, whatever the block size?
At byte 1024; its magic 0xEF53 is at byte 1080 (53 ef, little-endian).
Q2
write() returned 0 errors. Is the data on the disk?
No: it is in dirty pages of the page cache. fsync waits until the disk has it.
Q3
After a crash, what does the ext4 journal replay?
Only committed transactions. lost.txt (never committed) was gone; kept.bin (fsync) came back.
3 / 32

## Slide 4: Three ways into the kernel
PART 1
On purpose, by mistake, or from outside.
4 / 32

## Slide 5: Every event that stops the CPU is one of four kinds
class | cause | sync? | returns to | examples (x86-64 Linux)
interrupt | a device, a timer, another CPU | async | the next instruction | disk done, key pressed, timer tick
trap | an instruction, on purpose | sync | the next instruction | syscall, int3 (breakpoint)
fault | an instruction that might be fixed | sync | the SAME instruction, again | page fault (Lecture 11.1), #GP, #UD
abort | a fatal hardware error | sync | never | machine check, double fault
A student raises a hand: to ask the teacher something: a trap (system call). Planned, at a known moment.
A student makes a mistake: the teacher must look at it: a fault. Fix it and try the same step again, or fail the student (SIGSEGV).
The phone rings: in the middle of a sentence: an interrupt. Finish the sentence, answer, then continue the lesson.
Book: CS:APP §8.1 (exceptions, four classes); Love, LKD Ch. 7
5 / 32

## Slide 6: Exceptions and the IDT
PART 2
256 numbered events; one table of handlers.
6 / 32

## Slide 7: Make the CPU raise exceptions on purpose (exc.c)
./exc (real; the same in the QEMU guest)
7 / 0 -> FPE si_code 1 trap 0 err 0x0
int3 -> TRAP si_code 128 trap 3 err 0x0
ud2 -> ILL si_code 2 trap 6 err 0x0
hlt (kernel only) -> SEGV si_code 128 trap 13 err 0x0
inb $0x60 (port I/O) -> SEGV si_code 128 trap 13 err 0x0
read *NULL -> SEGV si_code 1 trap 14 err 0x4
write "hello" (rodata) -> SEGV si_code 2 trap 14 err 0x7
call code on the stack -> SEGV si_code 2 trap 14 err 0x15
exc.c: the handler (core lines)
void handler(int sig, siginfo_t *si,
void *ctx) {
ucontext_t *uc = ctx;
… uc->uc_mcontext
.gregs[REG_TRAPNO]
… .gregs[REG_ERR]
write(1, m, n);
_exit(0);
}
trap: the CPU's exception number (vector): 0 #DE, 3 #BP, 6 #UD, 13 #GP, 14 #PF
err: an error code the CPU pushes for some exceptions; for #PF it says why (slide 11)
si_code 128: SI_KERNEL: the kernel sent the signal without details (int3, #GP)
7 / 32

## Slide 8: The IDT: an array of 256 handler addresses
arch/x86/include/asm/trapnr.h (real)
7 #define X86_TRAP_DE 0 /* Divide-by-zero */
10 #define X86_TRAP_BP 3 /* Breakpoint */
13 #define X86_TRAP_UD 6 /* Invalid Opcode */
15 #define X86_TRAP_DF 8 /* Double Fault */
20 #define X86_TRAP_GP 13 /* General Protection */
21 #define X86_TRAP_PF 14 /* Page Fault */
25 #define X86_TRAP_MC 18 /* Machine Check */
arch/x86/kernel/idt.c (real lines)
65 SYSG(X86_TRAP_BP, asm_exc_int3),
71 INTG(X86_TRAP_PF, asm_exc_page_fault),
84 static const … struct idt_data def_idts[] = {
85 INTG(X86_TRAP_DE, asm_exc_divide_error),
88 INTG(X86_TRAP_UD, asm_exc_invalid_op),
94 INTG(X86_TRAP_GP, asm_exc_general_protection),
108 ISTG(X86_TRAP_MC, asm_exc_machine_check, …),
0 – 31 exceptions, fixed by Intel
32 – 235 device interrupts (FIRST_EXTERNAL_VECTOR 0x20)
0x80 old 32-bit int $0x80 system call (Lecture 9)
0xec – 0xff local timer 0xec, IPIs (reschedule 0xfd), spurious 0xff
C link: think of void (*idt[256])(void);. The CPU does idt[vector]() by itself. The kernel fills the table at boot; the IDTR register holds its address (lidt).
Book: Bovet & Cesati Ch. 4 (interrupts and exceptions); Love, LKD Ch. 7
8 / 32

## Slide 9: What the CPU does by itself, before any kernel code runs
1
Finish the current instruction (interrupt) or stop it (fault)
2
Look up IDT[vector]; check the gate's privilege level
3
From user mode: switch to this thread's kernel stack (address from the TSS)
4
Push SS, RSP, RFLAGS, CS, RIP (and an error code for some exceptions)
5
Interrupt gate: clear IF (no more interrupts on this CPU); jump to the handler
6
Handler done: iretq pops the five values and the program continues
arch/x86/include/asm/ptrace.h (real)
59 struct pt_regs {
… r15 … ax: saved by the kernel's entry code
84 unsigned long orig_ax; /* err code, IRQ, nr */
85 /* Return frame for iretq */
86 unsigned long ip;
87 unsigned long cs;
88 unsigned long flags;
89 unsigned long sp;
90 unsigned long ss;
SAME AS C
A function call, with more saved
call pushes only the return address; an exception pushes 5 values and switches stacks. iretq is the matching ret. And as with setjmp/longjmp, the saved registers can be changed before returning (Lecture 10.2's signal frames).
Book: Bovet & Cesati §4.2; Intel SDM Vol. 3, Ch. 6
9 / 32

## Slide 10: From the CPU's #DE to your SIGFPE: the kernel's side
arch/x86/kernel/traps.c (real lines)
194 DEFINE_IDTENTRY(exc_divide_error)
195 {
196 do_error_trap(regs, 0, "divide error", X86_TRAP_DE,
197 SIGFPE, FPE_INTDIV, error_get_trap_addr(regs));
198 }
…
149 do_trap(int trapnr, int signr, char *str, struct pt_regs *regs, …)
154 if (!do_trap_no_signal(tsk, trapnr, str, regs, error_code))
155 return; /* in the kernel: fix up or die */
157 show_signal(tsk, signr, "trap ", str, regs, error_code);
159 if (!sicode)
160 force_sig(signr); /* si_code SI_KERNEL */
161 else
162 force_sig_fault(signr, sicode, addr);
dmesg (no handler installed; real)
traps: t2[392] trap divide error
ip:557bf2e2716a sp:7ffdfb7cb4c0 error:0
in t2[116a,557bf2e27000+1000]
1
CPU: #DE → IDT[0] → asm_exc_divide_error
2
exc_divide_error → do_error_trap → do_trap
3
In user mode: a signal, SIGFPE, si_code FPE_INTDIV (1)
4
On the way back to user mode: the handler runs, or the default kills (Lecture 10.2)
If the divide happens inside the kernel there is no process to blame: do_trap_no_signal fixes it up, or the kernel prints an oops and dies.
Book: Love, LKD Ch. 7
10 / 32

## Slide 11: The page-fault error code: why did it fault?
arch/x86/include/asm/trap_pf.h (real)
18 X86_PF_PROT = 1 << 0, /* 0: not present */
19 X86_PF_WRITE = 1 << 1, /* 0: read */
20 X86_PF_USER = 1 << 2, /* 0: kernel mode */
21 X86_PF_RSVD = 1 << 3,
22 X86_PF_INSTR = 1 << 4, /* instruction fetch */
23 X86_PF_PK = 1 << 5,
1
INSTR (1)
0
RSVD (1)
1
USER (1)
0
WRITE (1)
1
PROT (1)
err 0x15 = 1 0 1 0 1: user, instruction fetch, page present (but not executable)
exc.c case | err | bits | meaning
read *NULL | 0x4 | USER | a user read of a page that is not there
write "hello" | 0x7 | USER WRITE PROT | the page is there (r--), writing is not allowed
code on the stack | 0x15 | USER INSTR PROT | the page is there (rw-), but NX: no execute
Lecture 11.1 again: SEGV_MAPERR (si_code 1) when PROT = 0, SEGV_ACCERR (si_code 2) when PROT = 1. The kernel decides from these bits and from the VMA.
The faulting address is not in the error code: the CPU puts it in register CR2, and exc_page_fault reads it first (read_cr2(), fault.c line 1512).
Book: Intel SDM Vol. 3 §4.7 (page-fault exceptions)
11 / 32

## Slide 12: Device interrupts
PART 3
From a disk's "done" to a woken process.
12 / 32

## Slide 13: Polling or interrupts: who waits for whom?
 | polling | interrupts
how | the CPU asks again and again: done? | the device tells the CPU when done
CPU while waiting | busy, asking | free: runs other programs, or sleeps (hlt)
delay after "done" | up to one polling interval | a few microseconds
good for | very fast devices (NVMe, 100 Gbit) | keyboard, disk, timer, USB, …
Analogy: waiting for a parcel. Polling: you walk to the gate every five minutes to look. Interrupts: the courier rings your phone. You can study in between.
device
raises a request: a wire (IRQ line) or a message (MSI/MSI-X)
I/O APIC / MSI
turns it into a vector number for one CPU
local APIC
in each CPU: queues vectors by priority, raises the CPU's interrupt pin
CPU
if IF = 1: finishes the instruction and uses IDT[vector]
Book: Love, LKD Ch. 7; Bovet & Cesati §4.2
13 / 32

## Slide 14: /proc/interrupts: every interrupt, counted per CPU
cat /proc/interrupts (QEMU guest, 1 CPU; real, shortened)
CPU0
0: 579 IO-APIC 2-edge timer
1: 9 IO-APIC 1-edge i8042
4: 18 IO-APIC 4-edge ttyS0
8: 1 IO-APIC 8-edge rtc0
14: 0 IO-APIC 14-edge ata_piix
25: 10 PCI-MSIX-0000:00:04.0 1-edge virtio0-req.0
NMI: 0 Non-maskable interrupts
LOC: 2328 Local timer interrupts
RES: 0 Rescheduling interrupts
CAL: 0 Function call interrupts
TLB: 0 TLB shootdowns
number: the IRQ number (not the vector); one column of counts per CPU
IO-APIC / PCI-MSIX who delivers it; edge or level ("fasteoi") triggering
the name given by the driver in request_irq: virtio0-req.0 is our disk, ttyS0 the serial console
LOC, RES, CAL, TLB CPU-local: timer ticks, and messages between CPUs (IPIs)
On a lab PC: ahci or nvme, xhci_hcd (USB), i915 …
Our 2-CPU test machine shows the same kinds of lines: virtio1-req.0 had 1973 interrupts on CPU 1.
Book: Love, LKD Ch. 7 (/proc/interrupts)
14 / 32

## Slide 15: How many per second? Watch them change
QEMU guest: ./irqtop while dd reads 64 MiB (real)
IRQ per second name
25 493 PCI-MSIX-0000:00:04.0 1-edge virtio0-req.0
LOC 351 Local timer interrupts
test machine (2 CPUs): ./irqtop, idle (real)
LOC 92 Local timer interrupts
CAL 25 Function call interrupts
49 3 … virtio7-input.0
QEMU guest, 5 seconds | LOC (timer) interrupts
idle (sleep 5) | 74
busy (yes > /dev/null) | 4926 ≈ 985 per second
Tickless (NO_HZ): a busy CPU gets a timer tick 1000 times a second (HZ = 1000, next part). An idle CPU programs its timer only for the next real event and sleeps: 15 ticks a second instead of 1000. That saves power.
1
Disk reading: about 500 disk interrupts a second, one for each finished batch of requests (read-ahead makes them bigger).
2
In the lab: run irqtop, then type, move the mouse, copy a file: watch which line wakes up.
15 / 32

## Slide 16: Inside the kernel: from vector to the driver's handler
__common_interrupt, function_graph (guest; real)
__common_interrupt() {
handle_edge_irq() {
irq_chip_ack_parent() { apic_ack_edge(); }
handle_irq_event() {
__handle_irq_event_percpu() {
vring_interrupt() {
virtblk_done() {
virtqueue_get_buf();
blk_mq_complete_request(); 421 us
virtqueue_enable_cb();
}
}
}
add_interrupt_randomness(); /* feeds /dev/random */
}
} 1560 us
arch/x86/kernel/irq.c (real lines)
247 DEFINE_IDTENTRY_IRQ(common_interrupt)
255 desc = __this_cpu_read(vector_irq[vector]);
256 if (likely(!IS_ERR_OR_NULL(desc))) {
257 handle_irq(desc, regs);
kernel/irq/handle.c (real line)
139 irqreturn_t __handle_irq_event_percpu(…)
158 res = action->handler(irq, action->dev_id);
1
vector → irq_desc (one per IRQ number)
2
flow handler (edge/level) → the driver's handler
Book: Love, LKD Ch. 7 (interrupt handlers)
16 / 32

## Slide 17: The whole story in one trace: request, interrupt, wake-up
ftrace events during readone /mnt/hello.txt, cold (QEMU guest; real, shortened)
readone [000] ..... 20.465358: block_rq_issue: 253,0 RM 4096 () 304 + 8 [readone]
<idle> [000] d.h1. 20.465556: irq_handler_entry: irq=25 name=virtio0-req.0
<idle> [000] d.h2. 20.465571: block_rq_complete: 253,0 RA () 296 + 8 [0]
<idle> [000] d.h2. 20.465600: block_rq_complete: 253,0 RM () 304 + 8 [0]
<idle> [000] dNh6. 20.465627: sched_wakeup: comm=readone pid=131
<idle> [000] dNh1. 20.465648: irq_handler_exit: irq=25 ret=handled
readone [000] ..... 20.466359: block_rq_issue: 253,0 RA 4096 () 164216 + 8 [readone]
… the same pattern for the data block, then read() returns 20 bytes
<idle>
the CPU was idle (hlt) when the disk interrupted: nobody waited actively
d
interrupts disabled on this CPU (IF = 0)
h
running in hard-interrupt context
N
"need resched": a better task (readone) is now runnable
17 / 32

## Slide 18: Watch one interrupt, from the disk to the woken process
Click the video to play or pause. About 1.4 minutes, no sound.
Watch for
1. The CPU sleeps in hlt; no polling.
2. APIC → vector → IDT entry.
3. IF = 0 while entering.
4. The driver's handler only completes and wakes.
5. iret or a switch to readone.
18 / 32

## Slide 19: The driver's side: request_irq registers a handler
include/linux/interrupt.h (real)
100 typedef irqreturn_t (*irq_handler_t)(int, void *);
164 static inline int __must_check
165 request_irq(unsigned int irq, irq_handler_t handler,
166 unsigned long flags, const char *name, void *dev)
168 return request_threaded_irq(irq, handler, NULL, …);
a handler, the usual shape (sketch)
static irqreturn_t mydev_irq(int irq, void *dev)
{
struct mydev *d = dev;
if (!(readl(d->regs + STATUS) & DONE))
return IRQ_NONE; /* not mine: shared line */
writel(DONE, d->regs + STATUS); /* acknowledge */
wake_up(&d->waitq);
return IRQ_HANDLED;
}
include/linux/irqreturn.h (real)
12 IRQ_NONE = (0 << 0),
13 IRQ_HANDLED = (1 << 0),
14 IRQ_WAKE_THREAD = (1 << 1),
QEMU guest trace (real)
irq_handler_entry: irq=4 name=ttyS0
irq_handler_exit: irq=4 ret=unhandled
SAME AS C
A callback, like signal()
You give the kernel a function pointer and a void * to pass back, as with qsort's compare or pthread_create. Lecture 14 writes kernel modules; Lecture 15 a driver that uses this.
Book: Love, LKD Ch. 7 (registering an interrupt handler)
19 / 32

## Slide 20: Top halves and bottom halves
PART 4
Do the urgent part now, with interrupts off; do the rest a little later.
20 / 32

## Slide 21: Interrupt context: be fast, never sleep
in a hard interrupt handler | why
no sleeping: no mutex_lock, no msleep | "current" is just whoever was interrupted
no copy_to_user / copy_from_user | they can page-fault and sleep; and whose memory would it be?
kmalloc only with GFP_ATOMIC | GFP_KERNEL may wait for memory to be freed
keep it short (microseconds) | IRQs are off on this CPU: other devices must wait
Analogy: a restaurant. The waiter takes your order at once and writes it on a slip (top half: fast, must not be missed). The kitchen cooks it a few minutes later (bottom half: the long work). If the waiter cooked every dish himself, the next customers would wait at the door.
1
Top half (the handler): acknowledge the device, take the data or the status, schedule the rest. Interrupts off.
2
Bottom half: everything else, later, with interrupts on: softirqs, tasklets, workqueues, threaded IRQs.
Same as Lecture 10.2: a signal handler only sets a flag; an interrupt handler does only the minimum. Same reason: it interrupts code at an unknown point.
Book: Love, LKD Ch. 7 (interrupt context), Ch. 8 (bottom halves)
21 / 32

## Slide 22: Softirqs: raised in the handler, run right after it
include/linux/interrupt.h (real)
550 HI_SOFTIRQ=0,
551 TIMER_SOFTIRQ,
552 NET_TX_SOFTIRQ,
553 NET_RX_SOFTIRQ,
554 BLOCK_SOFTIRQ,
555 IRQ_POLL_SOFTIRQ,
556 TASKLET_SOFTIRQ,
557 SCHED_SOFTIRQ,
558 HRTIMER_SOFTIRQ,
559 RCU_SOFTIRQ,
QEMU guest, 2 CPUs: events softirq_* and timer (real)
<idle> [000] d.h1. softirq_raise: vec=1 [action=TIMER]
<idle> [000] d.h1. softirq_raise: vec=7 [action=SCHED]
<idle> [000] ..s1. softirq_entry: vec=1 [action=TIMER]
<idle> [000] ..s1. timer_expire_entry: …
function=blk_stat_timer_fn
<idle> [000] ..s1. softirq_exit: vec=1 [action=TIMER]
<idle> [001] ..s1. timer_expire_entry: …
function=process_timeout
raise: in the hard handler (d.h): just set a bit "TIMER pending"
run: when the hard handler returns: interrupts back ON (..s), still not a process
overload: if softirqs keep coming, the rest moves to a thread per CPU: ksoftirqd/0, ksoftirqd/1
/proc/softirqs counts them per CPU. process_timeout = a sleeping process's timer expired: the softirq wakes it.
Book: Love, LKD Ch. 8 (softirqs)
22 / 32

## Slide 23: Four ways to do the rest later
mechanism | runs in | may sleep? | used for
softirq | interrupt context, right after the handler | no | network packets, timers, block completion: fixed list, very fast
tasklet | a softirq (TASKLET_SOFTIRQ) | no | older drivers; one function, never on two CPUs at once
workqueue | a kernel thread (kworker/…) | yes | most driver work: can take mutexes, allocate with GFP_KERNEL
threaded IRQ | its own kernel thread (irq/N-name) | yes | slow buses (I2C sensors), real-time kernels
ps in the QEMU guest (real, shortened)
16 0 [ksoftirqd/0]
24 0 [ksoftirqd/1]
41 0 [irq/9-acpi] # a threaded IRQ
9 0 [kworker/0:1-pm] # a workqueue worker
Rule of thumb for driver writers: need to sleep → workqueue (or a threaded IRQ). Must be fast and frequent → softirq or tasklet. The square brackets in ps mean kernel threads: no user memory at all.
Book: Love, LKD Ch. 8 (bottom halves and deferring work)
23 / 32

## Slide 24: Timers
PART 5
The timer interrupt: ticks, jiffies, and sleeping exactly (almost).
24 / 32

## Slide 25: The timer interrupt: the kernel's heartbeat
arch/x86/kernel/apic/apic.c (real lines)
1076 DEFINE_IDTENTRY_SYSVEC(sysvec_apic_timer_interrupt)
1080 apic_eoi();
1081 trace_local_timer_entry(LOCAL_TIMER_VECTOR);
1082 local_apic_timer_interrupt();
function_graph, QEMU guest (real, shortened)
__sysvec_apic_timer_interrupt() {
hrtimer_interrupt() {
ktime_get_update_offsets_now();
__hrtimer_run_queues() {
tick_nohz_highres_handler(); 87.6 us
}
tick_program_event(); /* set the next one */
} 186 us
QEMU guest: measuring HZ (real)
jiffies 4294670395 -> 4294675437
uptime 3.59 s -> 8.62 s
5042 ticks / 5.03 s = 1002 per second: HZ = 1000
The tick does: update jiffies and the time of day, charge CPU time to the running process (Lecture 8.1's scheduler), run expired timers (TIMER softirq).
jiffies: a counter of ticks since boot; kernel timeouts are in jiffies. It starts near 2³² − 300 000 on purpose, so wrap-around bugs show up in the first 5 minutes.
hrtimers: high-resolution timers in nanoseconds: nanosleep, timerfd, and the tick itself are hrtimers.
Book: Love, LKD Ch. 11 (timers and time management)
25 / 32

## Slide 26: Sleep 1 ms: how long does it really take?
slack.c (core lines)
struct timespec ms = { 0, 1000000 }; /* 1 ms */
for (i = 0; i < 1000; i++) {
t = now_us(); nanosleep(&ms, NULL);
late = now_us() - t - 1000; … }
prctl(PR_SET_TIMERSLACK, 1, 0, 0, 0); /* 1 ns */
./slack (test machine; real, two runs)
timer slack: 50000 ns
default slack (50 us) late by 99.3 us on average, worst 703.8 us
slack 1 ns late by 52.1 us on average, worst 2143.9 us
(run 2: 106.5 us and 51.8 us)
1
nanosleep sets an hrtimer; the process sleeps
2
The kernel may fire it up to timer slack (50 µs) late, to group wake-ups and let the CPU sleep longer
3
Then the timer interrupt, the wake-up and the scheduler add tens of µs more
4
Worst cases are ms: other work, or the host of our virtual machine
C link: sleep(1) and nanosleep promise a minimum time, never an exact one.
Book: Kerrisk, TLPI Ch. 23 (timers and sleeping)
26 / 32

## Slide 27: irqtop.c: a top for interrupts
LAB 13
Parse /proc/interrupts twice, one second apart, and sort the differences.
27 / 32

## Slide 28: Lab 13 tasks, step by step
1
TODO 1 in irqtop_starter.c: read the header line; count "CPU" with strstr → ncpu
2
TODO 2: for each line: the id before ':', the sum of up to ncpu numbers (strtoull), the name
3
TODO 3: match lines of the two snapshots by id (strcmp); count = after − before
4
TODO 4: qsort by count, biggest first; print the top 10
5
Run it idle; then type, copy a big file, run yes > /dev/null: which lines change?
Careful: the lines ERR and MIS have only ONE number, not one per CPU. strtoull tells you when it found no number: end == p.
reference, real
$ ./irqtop # test machine, idle
IRQ per second name
LOC 92 Local timer interrupts
CAL 25 Function call interrupts
49 3 … virtio7-input.0
$ ./irqtop 6 # while reading files
IRQ per second name
37 138 … virtio1-req.0
LOC 92 Local timer interrupts
CAL 26 Function call interrupts
$ ./irqtop # QEMU guest, dd
25 493 … virtio0-req.0
LOC 351 Local timer interrupts
28 / 32

## Slide 29: Checkpoint: test yourself
Q1
A page fault returns to which instruction? A system call?
→ the same one (fault, retried) / the next one (trap)
Q2
What does the CPU push on the kernel stack for an interrupt from user mode?
→ SS, RSP, RFLAGS, CS, RIP (+ error code for some exceptions)
Q3
exc printed trap 13 for hlt. Which exception, and which signal?
→ #GP, general protection → SIGSEGV
Q4
Why may an interrupt handler not call mutex_lock?
→ it may sleep, and there is no process to put to sleep
Q5
An idle CPU got 74 timer interrupts in 5 s with HZ = 1000. Why?
→ tickless idle (NO_HZ): no periodic tick when idle
29 / 32

## Slide 30: Key ideas from today
Interrupts are async (devices, timers); traps, faults and aborts come from the instruction itself.
The IDT maps 256 vectors to handlers; the CPU pushes SS, RSP, RFLAGS, CS, RIP and switches stacks.
Device → APIC → vector → irq_desc → the driver's handler, which completes work and wakes processes.
Top half fast with IRQs off; softirqs, workqueues, threads later. The timer tick: HZ, tickless, hrtimers.
30 / 32

## Slide 31: Homework 13 (due before Lecture 14.1)
1. Error codes
pferr.c makes 4 page faults: write *NULL, call address 0, write into main's code, read a kernel address. Predict each err value with trap_pf.h; run it; explain any surprise (fault.c, sanitize_error_code).
2. Ticks
On a lab PC, run irqtop idle and while one yes > /dev/null runs per CPU. Compare LOC with HZ × CPUs (grep CONFIG_HZ= /boot/config-$(uname -r)). Explain.
3. Timer slack
Run slack.c on a lab PC. Why is the average about 50 µs smaller with slack 1 ns? Why does the kernel add slack at all?
4. irqtop, live
Make irqtop refresh every second until Ctrl-C, like top: clear the screen with "\033[H\033[J", and stop cleanly with a SIGINT handler that only sets a flag.
5. Read the source
Follow #DE from the IDT to your SIGFPE: idt.c, traps.c (exc_divide_error, do_error_trap, do_trap). Why does int3 give si_code 128 but ud2 gives 2?
31 / 32

## Slide 32: Next lecture and reading
NEXT: LECTURE 14.1
Loadable kernel modules
Your first code inside the kernel: module_init and module_exit, printk and dmesg, insmod, lsmod and rmmod, module parameters, and why we do it inside a virtual machine.
Main text
R. Love, LKD, Ch. 7–8 and 11 today; Ch. 17 (devices and modules) for 14.1.
Driver book
Corbet, Rubini & Kroah-Hartman, Linux Device Drivers, 3rd ed. (free online), Ch. 2 (building and running modules).
CS:APP
§8.1 (exceptions) today; the kernel module chapters build on Lectures 7–13.
Lab files
lab13_files.zip: irqtop_starter.c, exc.c, slack.c, pferr.c.
32 / 32