## Slide 1
CSE 4105 · SYSTEM PROGRAMMING
Lecture 15.1
Character Device Drivers
your own file in /dev
Md Mahbub E Noor
Assistant Professor, Department of CSE
University of Barishal
QEMU guest (real)
$ insmod sysbuf.ko
$ echo hello from user space > /dev/sysbuf
$ cat /dev/sysbuf
hello from user space
# the bytes lived in a C array inside the kernel

## Slide 2: What you will learn today
Explain how a device file (c, major, minor) leads the kernel to one driver.
Write a char driver: register a number, a cdev and file_operations; make /dev/sysbuf.
Implement read and write with copy_to_user / copy_from_user, f_pos and EOF.
Design ioctl commands with _IO/_IOR and use them from a C program.
Today's plan (60 min)
0–5
Recap of 14.2
5–12
Device files
12–24
Writing the driver
24–38
open, read, write
38–48
ioctl
48–60
Lab, checkpoint
Lab 15.1: sysbuf.c, a 4 KiB device.
2 / 29

## Slide 3: Quick recap of Lecture 14.2
Q1
ls -l /dev/vda shows "b … 253, 0". What do b, 253 and 0 mean?
Block device; major 253 picks the driver (virtblk), minor 0 picks the device (the first disk).
Q2
Who calls a driver's probe function, and when?
The bus, when its match function pairs the driver with a device (platform: by name).
Q3
Who makes the file in /dev when a device appears?
devtmpfs (and udev), from the kernel's uevent: MAJOR, MINOR, DEVNAME.
3 / 29

## Slide 4: Devices are files
PART 1
A name, a letter and two numbers: the kernel does the rest.
4 / 29

## Slide 5: Three kinds of device, two of them in /dev
kind | talks in | seek? | examples | in /dev?
character | a stream of bytes | maybe | serial port, keyboard, /dev/null, a sensor | c …
block | fixed blocks (512 B sectors) | always | disks, SSDs, USB sticks, our RAM disk (15.2) | b …
network | packets | no | eth0, wlan0 | no: sockets instead
ls -l /dev/… (QEMU guest, real)
crw------- 1 0 0 1, 1 /dev/mem
crw-rw-rw- 1 0 0 1, 3 /dev/null
crw-rw-rw- 1 0 0 5, 0 /dev/tty
crw------- 1 0 0 4, 64 /dev/ttyS0
crw-rw-rw- 1 0 0 1, 9 /dev/urandom
crw-rw-rw- 1 0 0 1, 5 /dev/zero
SAME AS C
open, read, write, close
The same four calls you use on a text file (Lecture 12.1) work on /dev/null and /dev/ttyS0.
Where the size column usually is, ls shows major, minor: these files hold no data at all, only two numbers.
Book: LDD3 Ch. 1 (classes of devices) and Ch. 3
5 / 29

## Slide 6: dev_t: major and minor packed into one number
include/linux/kdev_t.h (real)
7 #define MINORBITS 20
8 #define MINORMASK ((1U << MINORBITS) - 1)
10 #define MAJOR(dev) ((unsigned int) ((dev) >> MINORBITS))
11 #define MINOR(dev) ((unsigned int) ((dev) & MINORMASK))
12 #define MKDEV(ma,mi) (((ma) << MINORBITS) | (mi))
241
major (12)
0
minor (20)
MKDEV(241, 0) = 241 << 20 = 0x0F100000
C link: shifts and masks, exactly like the permission bits of Lecture 12 and the ioctl numbers later today.
cat /proc/devices (real, start)
Character devices:
1 mem
4 /dev/vc/0
4 tty
4 ttyS
5 /dev/tty
5 /dev/console
10 misc
13 input
241 sysbuf # after insmod sysbuf.ko
Fixed or free? Old drivers own a fixed major (1, 4, 5). New drivers ask the kernel for a free one: we got 241. Never hard-code it: read it from /proc/devices or sysfs.
Book: LDD3 Ch. 3 (major and minor numbers)
6 / 29

## Slide 7: The name does not matter; the numbers do (real experiment)
QEMU guest, as root (real)
$ insmod sysbuf.ko; echo "made by mknod" > /dev/sysbuf
$ mknod /tmp/other c 241 0
crw-r--r-- 1 0 0 241, 0 /tmp/other
$ cat /tmp/other
made by mknod
$ mknod /tmp/minor1 c 241 1; cat /tmp/minor1
cat: can't open '/tmp/minor1': No such device or address
$ rmmod sysbuf; cat /tmp/other
cat: can't open '/tmp/other': No such device or address
$ ls -l /tmp/other
crw-r--r-- 1 0 0 241, 0 /tmp/other # still there
1
any name, in any directory: same major and minor, same driver, same data
2
minor 1: the driver registered only minor 0 → ENXIO
3
driver gone: the inode stays, but nobody owns 241 → ENXIO
Lecture 12.1 link: the inode of a device file stores the type and i_rdev = 241:0 instead of block pointers. open() looks the number up; the path is forgotten.
7 / 29

## Slide 8: Writing a char driver
PART 2
sysbuf: a 4 KiB buffer in the kernel that behaves like a small file.
8 / 29

## Slide 9: Four steps make /dev/sysbuf appear (sysbuf_init)
sysbuf.c: init (core lines)
static dev_t devno; static struct cdev cdev; static struct class *cls;
err = alloc_chrdev_region(&devno, 0, 1, "sysbuf"); /* free major */
if (err) return err;
cdev_init(&cdev, &sysbuf_fops);
err = cdev_add(&cdev, devno, 1); /* open() can reach us */
if (err) goto undo_region;
cls = class_create("sysbuf"); /* /sys/class/sysbuf */
if (IS_ERR(cls)) { err = PTR_ERR(cls); goto undo_cdev; }
device_create(cls, NULL, devno, NULL, "sysbuf"); /* uevent */
return 0;
undo_cdev: cdev_del(&cdev);
undo_region: unregister_chrdev_region(devno, 1);
return err;
1
a number: alloc_chrdev_region → 241:0 (char_dev.c 236)
2
a cdev: our file_operations, added to the kernel's table for 241:0 (cdev_add, line 479)
3
a class: a directory in /sys/class (Lecture 14.2)
4
a device: sends the uevent; devtmpfs makes /dev/sysbuf
exit does the same four, in reverse.
Book: LDD3 Ch. 3 (char device registration)
9 / 29

## Slide 10: struct file_operations: the driver's answer to every system call
include/linux/fs.h (real, part)
1983 struct file_operations {
1984 struct module *owner;
1985 loff_t (*llseek) (struct file *, loff_t, int);
1986 ssize_t (*read) (struct file *, char __user *, size_t, loff_t *);
1987 ssize_t (*write) (struct file *, const char __user *, size_t, loff_t *);
1994 long (*unlocked_ioctl) (struct file *, unsigned int, unsigned long);
… open, release, mmap, poll, fsync … (about 30 in all)
sysbuf.c (real)
static const struct file_operations sysbuf_fops = {
.owner = THIS_MODULE,
.open = sysbuf_open,
.read = sysbuf_read,
.write = sysbuf_write,
.llseek = default_llseek,
.unlocked_ioctl = sysbuf_ioctl,
};
user calls | kernel calls
open("/dev/sysbuf", …) | sysbuf_open
read(fd, buf, n) | sysbuf_read
write(fd, buf, n) | sysbuf_write
lseek(fd, 14, SEEK_SET) | default_llseek
ioctl(fd, cmd, arg) | sysbuf_ioctl
close(fd) | .release (none: nothing to do)
SAME AS C
A table of function pointers
Like qsort's comparator, or a struct of callbacks in your own C: the kernel calls f->f_op->read(…) without knowing who wrote it. Missing entries are NULL; the kernel then uses a default or returns an error.
10 / 29

## Slide 11: After insmod sysbuf.ko: the number, the node, the sysfs entry (real)
QEMU guest (real)
$ insmod sysbuf.ko; dmesg | tail -1
sysbuf: ready as /dev/sysbuf, major 241 minor 0
$ ls -l /dev/sysbuf
crw------- 1 0 0 241, 0 Oct 15 04:52 /dev/sysbuf
$ grep sysbuf /proc/devices
241 sysbuf
the sysfs side (real)
$ cat /sys/class/sysbuf/sysbuf/dev
241:0
$ cat /sys/class/sysbuf/sysbuf/uevent
MAJOR=241
MINOR=0
DEVNAME=sysbuf
$ readlink -f /sys/class/sysbuf/sysbuf
/sys/devices/virtual/sysbuf/sysbuf
1
device_create → uevent with MAJOR=241 MINOR=0 DEVNAME=sysbuf (the same three lines as the uevent file)
2
devtmpfs makes /dev/sysbuf, mode crw------- (root only); on a desktop, udev may then change owner and mode by its rules
11 / 29

## Slide 12: open, read, write
PART 3
From a file descriptor to our functions, and bytes across the user/kernel border.
12 / 29

## Slide 13: How open("/dev/sysbuf") finds our driver
fs/char_dev.c (real lines, shortened)
373 static int chrdev_open(struct inode *inode, struct file *filp)
381 p = inode->i_cdev; /* cached from an earlier open? */
382 if (!p) {
386 kobj = kobj_lookup(cdev_map, inode->i_rdev, &idx);
387 if (!kobj)
388 return -ENXIO;
395 inode->i_cdev = p = new;
} else if (!cdev_get(p)) /* try_module_get */
fops = fops_get(p->ops);
412 replace_fops(filp, fops); /* f_op = &sysbuf_fops */
413 if (filp->f_op->open) {
414 ret = filp->f_op->open(inode, filp);
452 const struct file_operations def_chr_fops = {
453 .open = chrdev_open, …
ftrace: cat /dev/sysbuf (real)
chrdev_open() {
_raw_spin_lock();
try_module_get();
_raw_spin_unlock();
try_module_get();
module_put();
sysbuf_open [sysbuf]();
}
The trick: every char device file starts with the same generic f_op (def_chr_fops). Its open looks up the number, then swaps in the driver's own table. From then on read() goes straight to sysbuf_read.
Book: LDD3 Ch. 3 (the file structure, open)
13 / 29

## Slide 14: Watch cat /dev/sysbuf, step by step
Click the video to play or pause. About 1.2 minutes, no sound.
Watch for
1. The inode only holds 241:0.
2. kobj_lookup finds the cdev.
3. replace_fops: f_op becomes ours.
4. copy_to_user moves 22 bytes.
5. read returns 0: EOF.
14 / 29

## Slide 15: sysbuf_read: give bytes from the current position, 0 at the end
sysbuf.c (real)
static ssize_t sysbuf_read(struct file *f, char __user *buf,
size_t count, loff_t *pos)
{
ssize_t n;
mutex_lock(&lock);
if (*pos >= used) { mutex_unlock(&lock); return 0; } /* EOF */
n = min(count, used - (size_t)*pos);
if (copy_to_user(buf, data + *pos, n)) {
mutex_unlock(&lock); return -EFAULT;
}
*pos += n;
mutex_unlock(&lock);
return n;
}
ftrace: vfs_read (real)
vfs_read() {
rw_verify_area() {
security_file_permission();
}
sysbuf_read [sysbuf]() {
mutex_lock();
__check_object_size();
mutex_unlock();
1
return n > 0: n bytes read; may be fewer than asked
2
return 0: end of file; cat stops
3
return −errno: read() gives −1 and sets errno
SAME AS C
The read() contract of Lecture 12.1
A regular file obeys exactly these rules. A driver that follows them works with cat, dd, C stdio.
15 / 29

## Slide 16: Why copy_to_user, and never memcpy into buf
 | memcpy(buf, data, n) | copy_to_user(buf, data, n)
buf is NULL | oops in the kernel | returns n (not copied) → −EFAULT
buf points into the kernel | user overwrites kernel memory! | rejected: not a user address
buf's page is swapped out | page fault in kernel code | fault handled, page brought in
SMAP on (modern x86) | fault: kernel may not touch user pages | opens the user window just for the copy
hwtest151: bad pointers (real)
write 3 bytes: 3
read into (nil): -1
(Bad address)
read into 0xffffffff81000000: -1
(Bad address)
write from 0xffffffff81000000: -1
(Bad address)
Lecture 9 and 13 link: "Bad address" is EFAULT. The kernel survived, because copy_to_user's faults go to a fix-up table instead of an oops.
The rule: a pointer that came from user space is a number the user chose. Check it and copy through it with copy_to_user, copy_from_user, get_user, put_user. They return the number of bytes not copied (0 = success).
Book: LDD3 Ch. 3 (read and write); Love, LKD Ch. 5 (system calls)
16 / 29

## Slide 17: sysbuf_write, and what a full device says
sysbuf.c (real, core lines)
if (*pos >= SYSBUF_SIZE) {
mutex_unlock(&lock);
return -ENOSPC; /* "No space left on device" */
}
n = min(count, SYSBUF_SIZE - (size_t)*pos);
if (copy_from_user(data + *pos, buf, n)) { … return -EFAULT; }
*pos += n;
if (*pos > used) used = *pos;
return n; /* may be less than count */
QEMU guest (real)
$ dd if=/dev/zero of=/dev/sysbuf bs=1024 count=5
dd: error writing '/dev/sysbuf':
No space left on device
5+0 records in
4+0 records out
$ cat /dev/sysbuf | wc -c
4096
1
writes 1–4: 1024 bytes each, f_pos 1024 → 4096. Write 5: f_pos is 4096 = SYSBUF_SIZE → −ENOSPC; dd reports it and stops
2
a write that only partly fits returns the smaller n: the caller must loop (Lecture 12.1's "short write"); stdio's fwrite does that for you
17 / 29

## Slide 18: sysbuf_open sees the flags: 0x8241 and 0x8000 (real)
dmesg (real)
$ echo "hello from user space" > /dev/sysbuf
sysbuf: open by init (pid 1), minor 0, flags 0x8241
$ cat /dev/sysbuf
sysbuf: open by cat (pid 88), minor 0, flags 0x8000
0x8000
LARGEFILE (1)
… (2)
0x200
TRUNC (1)
… (2)
0x40
CREAT (1)
… (2)
0x1
WRONLY (1)
0x8241 = O_LARGEFILE | O_TRUNC | O_CREAT | O_WRONLY (the shell's >)
0x8000 = O_LARGEFILE | O_RDONLY (0) (cat)
sysbuf_open (real)
if ((f->f_flags & O_ACCMODE) != O_RDONLY
&& (f->f_flags & O_TRUNC)) {
mutex_lock(&lock); used = 0;
mutex_unlock(&lock);
}
SAME AS C
fopen("f", "w") truncates
The shell's > is open(…, O_WRONLY|O_CREAT|O_TRUNC). For a regular file the file system truncates; for a device, only if the DRIVER decides to: we do.
O_CREAT on a device? The node already exists, so the flag does nothing. The driver sees all flags and may honour the ones that mean something for it (O_TRUNC, O_NONBLOCK: Homework 15.1).
18 / 29

## Slide 19: An open file keeps the module loaded: .owner = THIS_MODULE
QEMU guest (real)
$ cat /sys/module/sysbuf/refcnt
0
$ (sleep 3 < /dev/sysbuf &); sleep 1
$ cat /sys/module/sysbuf/refcnt
1
$ rmmod sysbuf
rmmod: can't unload module 'sysbuf': Resource temporarily unavailable
$ sleep 3; rmmod sysbuf; echo $?
0
1
sleep's stdin is /dev/sysbuf: an open struct file
2
chrdev_open took a reference: try_module_get
3
rmmod refuses: EAGAIN while refcnt > 0
4
sleep exits, file closed, module_put: rmmod works
Without .owner, rmmod would succeed while sleep still holds the file. Its next read would jump to sysbuf_read, which is no longer in memory: an oops, like forgetting remove_proc_entry in Lab 14.1. The kernel protects you only if you fill in .owner.
19 / 29

## Slide 20: ioctl: everything that is not read or write
PART 4
Commands with numbers, and a header shared by the driver and its programs.
20 / 29

## Slide 21: An ioctl command is a 32-bit number with four fields
sysbuf.h (shared by driver and programs)
#include <linux/ioctl.h>
#define SYSBUF_MAGIC 'S'
#define SYSBUF_CLEAR _IO(SYSBUF_MAGIC, 1)
#define SYSBUF_GETSIZE _IOR(SYSBUF_MAGIC, 2, int)
include/uapi/asm-generic/ioctl.h (real)
23 #define _IOC_NRBITS 8
24 #define _IOC_TYPEBITS 8
32 #define _IOC_SIZEBITS 14
36 #define _IOC_DIRBITS 2
66 #define _IOC_READ 2U
86 #define _IOR(type,nr,size) _IOC(_IOC_READ,(type),(nr),…)
10 = READ
dir (2)
4 = sizeof(int)
size (14)
0x53
type ('S') (8)
2
nr (8)
SYSBUF_GETSIZE = 2 << 30 | 4 << 16 | 0x53 << 8 | 2 = 0x80045302 (sbtest printed exactly this)
Why encode? The number says which way data flows and how much, so tools (strace) and the kernel can check it; the magic letter keeps one driver's numbers apart from another's.
Book: LDD3 Ch. 6 (ioctl, choosing the numbers)
21 / 29

## Slide 22: sysbuf_ioctl, and a C program that uses all of it
sysbuf.c (real)
static long sysbuf_ioctl(struct file *f,
unsigned int cmd, unsigned long arg)
{
int size;
switch (cmd) {
case SYSBUF_CLEAR: … used = 0; … return 0;
case SYSBUF_GETSIZE: size = used;
return put_user(size, (int __user *)arg);
default: return -ENOTTY;
}
}
./sbtest (real)
/* write 22 bytes, GETSIZE, lseek 14, read twice, bad ioctl */
write: 22 bytes, size now 22
read at offset 14: 8 bytes "Barishal"
read again: 0 (end of file)
ioctl 0x1234: Inappropriate ioctl for device
SYSBUF_GETSIZE = 0x80045302 (_IOR('S', 2, int))
ftrace: one ioctl (real)
__x64_sys_ioctl() {
__fdget(); security_file_ioctl(); do_vfs_ioctl();
sysbuf_ioctl [sysbuf]() { mutex_lock(); mutex_unlock(); }
ENOTTY = "Inappropriate ioctl for device": the historic name, from the days when ioctl was mostly for terminals. In the same trace, printf's isatty() check went to tty_ioctl, not to us.
22 / 29

## Slide 23: Two programs, two CPUs, one buffer: why sysbuf has a mutex
time | CPU 0: writer (echo) | CPU 1: reader (cat)
t1 | *pos 0 < 4096, n = 22 | 
t2 | copy_from_user … (page fault: sleeps!) | *pos 0 < used ?
t3 |  | used is still old: reads half-written data
t4 | used = 22 | 
1
copy_*_user may sleep (the user page may need to be read from disk)
2
so the lock must allow sleeping: a mutex; a spinlock waiter never sleeps, and a holder must not (Lecture 13)
3
hold it around every access to data and used, and unlock on every return path
SAME AS C
Lecture 10.1's race, again
Two processes, one counter, fixed with a semaphore. Kernel version: DEFINE_MUTEX(lock); mutex_lock(&lock); … mutex_unlock(&lock);
Forget one unlock (e.g. on the −EFAULT path) and the next reader sleeps forever in mutex_lock: the process cannot even be killed with Ctrl-C. Check every return in the lab code.
23 / 29

## Slide 24: sysbuf.c: your own /dev file
LAB 15.1
Register, read, write, ioctl; test with echo, cat, dd and sbtest.
24 / 29

## Slide 25: Lab 15.1 tasks, step by step
1
cd lab15_1; make builds sysbuf_starter.ko and the static test program sbtest
2
TODO 1 init: alloc_chrdev_region, cdev_init/cdev_add, class_create, device_create (with the goto ladder)
3
TODO 2 read: EOF, min, copy_to_user, *pos += n
4
TODO 3 write: −ENOSPC, copy_from_user, update used
5
TODO 4 ioctl: CLEAR, GETSIZE with put_user, default −ENOTTY
6
../guest/run_guest.sh . then insmod, echo, cat, dd, ./sbtest
the starter, before TODO 1 (real)
$ insmod sysbuf_starter.ko; echo status $?
insmod: can't insert 'sysbuf_starter.ko': No such device
status 19
$ dmesg | grep sysbuf
sysbuf: not registered yet: TODO 1
the finished lab (real)
$ ./sbtest
write: 22 bytes, size now 22
read at offset 14: 8 bytes "Barishal"
read again: 0 (end of file)
ioctl 0x1234: Inappropriate ioctl for device
SYSBUF_GETSIZE = 0x80045302 (_IOR('S', 2, int))
25 / 29

## Slide 26: Checkpoint: test yourself
Q1
ls -l shows "crw------- … 241, 0 /tmp/x". Which driver runs when you cat it?
→ whoever registered char major 241, minor 0 (sysbuf)
Q2
Your read function returns 0. What does cat do?
→ it sees end of file and stops
Q3
Why may a driver not memcpy into the read buffer?
→ it is a user address: use copy_to_user (EFAULT, page faults, SMAP)
Q4
Decode _IOR('S', 2, int).
→ dir READ, size 4, type 0x53, nr 2 = 0x80045302
Q5
rmmod fails with EAGAIN although nobody uses the driver's API. Why?
→ a process still has the device file open (owner refcount)
26 / 29

## Slide 27: Key ideas from today
A device file is a name for (c, major, minor); the number finds a cdev, the cdev holds file_operations.
init: number → cdev_add → class → device_create (uevent makes /dev); exit undoes it in reverse.
read/write follow the file contract: bytes, f_pos, 0 = EOF, −errno; copy_*_user for user memory.
ioctl numbers encode direction, size, type and number; unknown commands return −ENOTTY.
27 / 29

## Slide 28: Homework 15.1 (due before Lecture 15.2)
1. Blocking read
Make read wait for data instead of returning 0 (wait_event_interruptible, wake_up_interruptible in write). Show that cat sleeps (state S, wchan). What happens on Ctrl-C, and with O_NONBLOCK?
2. ioctl numbers
Compute SYSBUF_CLEAR = _IO('S', 1) in hex. printf's isatty() sent TCGETS = 0x5401: decode its four fields. Why was it _IO-style, not _IOR?
3. Open flags
hwtest151's opens printed flags 0x8800 and 0x8202. Decode both. Which of these flags does sysbuf_open act on?
4. ENXIO
With fs/char_dev.c (lines 373–414) explain both ENXIO results of slide 7: minor 1, and the node after rmmod.
5. copy_to_user
Explain each "Bad address" on slide 16, and why the kernel did not oops. What does copy_to_user return?
28 / 29

## Slide 29: Next lecture and reading
NEXT: LECTURE 15.2
Block device drivers
Disks talk in sectors and requests, not bytes: bios, the request queue (blk-mq), the page cache in front of it. Lab: a RAM disk that you format with ext2 and mount.
Driver book
Corbet, Rubini & Kroah-Hartman, LDD3 (free), Ch. 3 and 6 today; Ch. 16 (block drivers) for 15.2: the ideas, but its API is old.
Kernel side
R. Love, LKD, Ch. 14 (the block I/O layer).
Source
Linux 6.8: fs/char_dev.c, include/linux/fs.h, cdev.h, kdev_t.h, uapi/asm-generic/ioctl.h (Linux v6.8 source online: elixir.bootlin.com/linux/v6.8).
Lab files
lab15_files.zip: lab15_1/ (sysbuf_starter.c, sysbuf.h, sbtest.c), guest/run_guest.sh.
29 / 29